## Slide 1
Project Seminar On
“AI-Based Smart Driver Monitoring & Accident Prevention System”
Partial fulfillment of Six Semester
Bachelor of Technology In COMPUTER ENGINEERING
Submitted By
Piyush Sondawale Sameer Meshram
Nayan Mandwalker
Under the Guidance of PROF . K . SARODE
DEPARTMENT OF COMPUTER ENGINEERING SMT. RADHIKATAI PANDAV COLLEGE OF ENGINEERING, NAGPUR Rashtrasant Tukdoji Maharaj Nagpur University, Nagpur
2024-2025
DEPARTMENT OF COMPUTER ENGINEERING

## Slide 2
INDEX TOPICS INTRODUCTION LITERATURE SURVEY EXITING WORK MODULES IMPLEMENTATION EXPERIMENTAL RESULT (OUTPUT & GRAPHS) CONCLUSION FUTURE SCOPE REFERENCES

## Slide 3
ABSTRACT
We present a real-time, vision-based smart driver monitoring and accident prevention system that monitors:
Eye movements
Blink frequency (EAR)
Mouth opening (MOR)
Head orientation (NLR).
The system links visual fatigue indicators to an adaptive safety algorithm that issues
Graded alerts
Recommends breaks
Keywords: Real-Time Drowsiness Detection, Facial Recognition Monitoring, Driver Safety Enhancement, Fatigue Alert System.

## Slide 4
AI-Based Smart Driver Monitoring & Accident Prevention System
Drowsy driving causes 70,000–80,000 crashes and 1,000–2,000 deaths worldwide annually. This system uses facial recognition and deep learning to detect fatigue in real time — and alert drivers before disaster strikes.
CHAPTER 1: INTRODUCTION

## Slide 5
CHAPTER 2: LITERATURE SURVEY
What Researchers Have Found
1
Dr. M. Ramya Devi
CNN + RNN for temporal eye/facial analysis — reduces false alarms in real-time fatigue detection.
2
Magán et al.
Deep learning on sequential image frames improves accuracy over single-frame detection.
3
Zambrano et al.
EAR + MAR with CNN detects fatigue, distraction & emotion under varied lighting conditions.
4
Krishna et al.
YOLO + Vision Transformers achieve ~96% accuracy — outperforming CNN-only models.
5
Kumar et al.
CNN-based blink rate & eye closure analysis optimized for real-time Indian road conditions.

## Slide 6
System Architecture
Three-Layer Design
Presentation Layer (UI)
Dashboard showing real-time alertness status, session data, drowsiness alerts, and break reminders.
Fatigue Detection Layer
Front camera captures eye closure, head position, and yawning — analyzed by CNN models to generate live fatigue scores.
Alert & Adaptation Layer
Dynamically adjusts alert intensity and assistance features based on detected fatigue level.
Fig 3.1 — EAR threshold decision flow: video input → facial landmarks → drowsy / not drowsy classification
CHAPTER 3: EXISTING WORK

## Slide 7
CHAPTER 4: MODULES
System Modules
UI & Control
Start/stop monitoring, live camera feed, and dashboard showing Safe / Drowsy / Distracted status with visual warnings. Built with Python (Streamlit).
Video Acquisition & Face Detection
Captures real-time frames via webcam or IP camera using OpenCV, isolating the facial region for downstream analysis.
Fatigue Detection
Calculates EAR (eye closure ≥ 2s = drowsy) and MAR (yawn detection) using facial landmark analysis.
Attention & Alert System
3D head pose estimation detects distraction (looking left/right/down). Triggers audio alarms, voice warnings & visual alerts.

## Slide 8
CHAPTER 5: IMPLEMENTATION
Core Code Highlights
Session Timer
Tracks elapsed driving time and displays it live using datetime.now() and Streamlit metrics.
WebRTC Camera Stream
Live video via webrtc_streamer with DrowsinessProcessor for real-time frame analysis.
Status Classification
Driver state (safe, drowsy, distracted, warning) drives color-coded UI alerts dynamically.
Active Mode Display
Shows Day/Night mode, yawn detection, face count, and CNN status in a live two-column panel.
sc = s.get("status_cls", "safe")
if sc == "safe":
st.success("
✅ DRIVER IS SAFE")elif sc == "drowsy": st.error("⚠️ DROWSY! WAKE UP!")elif sc == "distracted": st.warning("⚠️ DISTRACTED!")elif sc == "warning": st.warning("⚡ LOW BLINK RATE!")else: st.info("❌ NO FACE DETECTED")

## Slide 9
CHAPTER 6: EXPERIMENTAL RESULTS
System Output & Detection
0.336
EAR (Normal)
Threshold: 0.160 — eye closure triggers drowsy alert
15.6%
PERCLOS
Eyes closed % in last 60s — alarm triggers at 20%
5/min
Blink Rate
Below 8/min triggers early drowsiness warning
17%
CNN Eye Closed
MobileNetV2 probability — Eyes Open confirmed
Fig 6.2: Real-time detection — green (Safe), red (Drowsy, eyes closed), yellow (Distracted, MOR: 0.68 yawning detected).
Eyes open, head forward. Green status. EAR normal, calibration active
✅ Safe
⚠️ Drowsy
Eyes closed detected. Red alert fires. EAR drops below threshold
⚡ Distracted
Yawning or gaze deviation. Yellow warning. MAR: 0.68 flagged

## Slide 10
CHAPTER 7: CONCLUSION
Conclusion
Adaptive & Personalized Safety
Unlike traditional alerts, this system personalizes interventions — improving reaction time and reducing crash risk.
Real-Time Fatigue Interpretation
Detects eye closure, head movements, and yawning to provide timely alerts and recommend breaks.
Privacy-First, On-Device
Local implementation ensures offline functionality and secure biometric data management — no cloud dependency.

## Slide 11
CHAPTER 8: FUTURE SCOPE
What's Next
IoT & Fleet Integration
Send instant alerts to family, fleet managers, or vehicle owners. Support commercial transport and public fleets.
Night Vision & Emotion AI
Infrared cameras for low-light monitoring; emotion and stress detection to prevent risky driver behavior.
Wearables & GPS
Heart rate monitoring via smart wearables; GPS tracking for emergency location alerts.
Vehicle Control Integration
Auto-reduce speed, apply brakes, or activate lane assist when critical drowsiness is detected.

## Slide 12
REFERENCES
1
Dr. M. Ramya Devi
CNN + RNN for temporal eye/facial analysis — reduces false alarms in real-time fatigue detection.
2
Magán et al.
Deep learning on sequential image frames improves accuracy over single-frame detection.
3
Zambrano et al.
EAR + MAR with CNN detects fatigue, distraction & emotion under varied lighting conditions.
4
Krishna et al.
YOLO + Vision Transformers achieve ~96% accuracy — outperforming CNN-only models.
5
Kumar et al.
CNN-based blink rate & eye closure analysis optimized for real-time Indian road conditions.

## Slide 13
Thank You